# Make fresh RNA sample buffer: (add bromophenol blue)

| 1.25X Sample buffer | Final | 2mls |
| --- | --- | --- |
| 10XMOPS buffer | 5 | 250 (l |
| 37% formaldehyde (12.3M) | 2.2M | 450 (l |
| deionized formamide | 50% | 1250 (l |
| glycerol | 2.3% | 57 |

Rinse glassware with RNAZap or 2% Absolve o/n, rinse: 3XddH20 and 1X DEPC H20.

Thaw RNA.

Prechill 0.5 ml tubes.

Water bath to 68(C.

Pour Gel:

Heat RNase free agarose in DEPC H20, cool to 50(C, add remaining reagents.

|  | Final | 300 mls |
| --- | --- | --- |
| RNAse-free agarose | 1% | 3 g |
| DEPC H20 |  | 243 ml |
| EtBr |  | 6 (l |
| 10X MOPS | 1X | 30 ml |
| 37% formaldehyde | 1.1 M | 27 ml |

*only use about 200 ml

# Prepare samples

- Pipet 20(g total RNA to 0.5 ml tube.

- Add sample buffer.

- Heat 68(C, 5 min.

- Chill on ice.

- Load samples under 1XMOPS ~1.5 L.

- Run gel at o/n 40V or ~6H 100V.

- Photograph with UV ruler.

- Cut off RNA ladder.

Transfer:  Follow directions for Nytran SuPerCharge TurboBlotter Transfer in 20XSSC (p8).

- Soak gel 10XSSC.

- Label and then wet Hybond membrane in DEPC-H20, then soak membrane in 20XSSC 5 min.

- Level stack tray.

- Stack cut paper towels ~2 inches.

- Place 20 sheets dry GB004 thick paper.

- Place 4 sheets dry GB002 thin paper on top of stack.

- Place one sheet prewet (20XSSC) GB002 on stack.

- Place transfer membrane on stack.

- Cover membrane with agarose gel; roll out any air bubbles with pipette.

- Cut top right corner of gel & membrane, do not flip gel to place on top of membrane.   Want bottom of the wells against the membrane.

- Use parafilm to cover excess blotting paper around gel.

- Wet the top of the gel with 20XSSC.

- Place 3 sheets prewet GB002 paper on stack.

- Attach buffer tray

- Fill the buffer tray with transfer buffer.

- Start transfer by applying precut, prewet buffer wick.

- Place the wick cover on top of the stack.

- Allow to transfer for o/n.

- Mark corners of gel, 28S, 18S, and wells on membrane.  Photograph membrane with UV ruler.

- Air dry RNA side up.

- While membrane is damp, UV cross-link RNA side towards UV bulbs Stratagene autocrosslink.

- Rinse in 2XSSC, shaking RT.

- Store dry in seal-a-meal bag at 4(C.